## Slide 1: Matlab tutorial Profile model exercise
Dano Roelvink

## Slide 2: Command line vs script
You can enter a command or expression on the command line, e.g.
  a=3
  b=4
  c=sqrt(a^2+b^2)
or you can put these commands in a script, save the script (*.m file) and execute the script from command line.
Try both options for this simple example

## Slide 3: Arrays
Arrays are 1-dimensional matrices
x=[0:0.1:10]
This creates an array ‘x’ with values 0,0.1,0.2,…9.9,10.
y=x.^2
This computes the square of each element of x. The dot is needed so the squaring is done for each element separately.
Another way of doing this is by a for-loop:
for i=1:length(x)
y(i)=x(i)^2
end
Notice that now no dot is required .
The function length returns the length of the array x.

## Slide 4: Plotting
You can plot the result by typing
figure(1)
An empty figure is opened or figure 1 is reopened.
plot(x,y)
Now you see a nice plot. You can add xlabel, ylabel, title and modify the line width;
plot(x,y,’linewidth’,2)
xlabel(‘x’)
ylabel(‘y’)
title(‘x^2’)

## Slide 5
Now add a second variable:
z=2*x.^2;
You can plot both lines as follows:
plot(x,y,x,z,’linewidth’,2)
xlabel(‘x’)
ylabel(‘y,z’)
title(‘x^2,2x^2’)
legend(‘x^2’,’2x^2’)
You can store all relevant commands in a script named for example x2.m, and execute it by simply typing ‘x2’.

## Slide 6
%% Script to plot parabolic function
x=[-10:0.1:10]
for i=1:length(x)
y(i)=x(i)^2
z(i)=2*x(i)^2
end
figure(1)
plot(x,y,x,z,’linewidth’,2)
xlabel(‘x’)
ylabel(‘y,z’)
title(‘x^2,2x^2’)
legend(‘x^2’,’2x^2’)

## Slide 7: Creating a depth profile and grid
clear all
dx=1;
% load the bottom profile points
xz=load('bottom.txt')
xp=xz(:,1);
zp=xz(:,2);
% create a grid with 1m resolution
x=[xp(1):dx:xp(end)];
% interpolate zp to grid
zb=interp1(xp,zp,x);
% now plot the result
figure;
plot(xp,zp,'o',x,zb,'.')
Bottom.txt:
File with
0 -0.5
10 -0.5
50 0.1

## Slide 8: Use functions for clarity
clear all
dx=.5; % grid size
zs=.1; % water level
hmin=0.1 % minimum water depth
T = 2; % wave period
% load the bottom profile points
xz=load('bottom.txt')
xp=xz(:,1);
zp=xz(:,2);
% create a grid with resolution dx
x=[xp(1):dx:xp(end)];
% interpolate zp to grid
zb=interp1(xp,zp,x);
% compute water depth
h=zs-zb;
h=max(h,hmin);
% compute k, C, Cg
[k,C,Cg]=disper(h,T);

## Slide 9: Example function disper
function [k,C,Cg]=disper(h,T)
g=9.81;
sigma=2*pi./T;
k = sigma.^2/g*(1-exp(-(sigma.*sqrt(h/g)).^2.5)).^(-0.4);
C= sigma./k;
n = 0.5+k.*h./sinh(2.*k.*h);
Cg=n.*C;
Guo (2002), see Fenton (2006)

## Slide 10: Plotting result
% now plot the result
figure(1)
subplot(4,1,1)
plot(xp,zp,'o',x,zb,'.')
legend('input points','grid')
ylabel('zb (m)')
title('Profile')
subplot(4,1,2)
plot(x,h,'r','linewidth',2)
ylabel('h (m)')
title('Water depth')
subplot(4,1,3)
plot(x,k,'r','linewidth',2)
ylabel('k (m^-^1)')
title('Wave number')
subplot(4,1,4)
plot(x,C,'b',x,Cg,'r','linewidth',2)
legend('C','Cg')
ylabel('C,Cg (m/s)')
xlabel('X (m)')
title('Celerity and group velocity')

## Slide 11: Refraction using Snel’s Law
Formula:
Matlab code:
theta=asind(sind(theta0)*C/C(1));
Angles in degrees, otherwise use sin and asin

## Slide 12: Solving 1D wave energy balance
Inside surf zone:
  Group velocity follows from dispersion relation
  Wave angle follows from Snel’s Law
  Dissipation follows from e.g. Baldock, relating wave dissipation to wave energy and water depth
  Solve E numerically, starting from known value outside breaker zone

## Slide 13: Solving 1D wave energy balance
Very simple numerical scheme:

## Slide 14: From discrete formula to code
Formula:
Snippet of code:
E(1)=1/8*rho*g*H0;
for i=1:length(x)-1
H(i)=sqrt(8*E(i)/rho/g);
Dw(i)=Baldock(gamma,k(i),h(i),H(i),T,opt);
E(i+1)=(E(i)*Cg(i)*cosd(theta(i))-Dw(i)*dx)/(Cg(i+1)*cosd(theta(i+1)));
end

## Slide 15: 2022 Assignment 1
Read x, zb profile from depth.tek (Boers 1996 experiment)
Water level is 0.75 m.
Tp=2.03 s
Read observed wave data from hrms.txt
Compute Hrms throughout the flume
Compare with observations in plot, with computed Hrms as drawn line and observations as dots
Find optimal value of gamma.
Bonus: compare Qb and C with values found in q.tek and c.tek
Write a brief report in groups of 2 students.