## Slide 1
Source: Rijkswaterstaat

## Slide 2: Three parts
Estuarine morphodynamics (3 periods)
  ppt in group
Salt intrusion and density currents (3 periods)
  assignments (no mark)
Harbour siltation (1 period)
  Homework Exercise: 20% of module mark

## Slide 3: Estuarine morphodynamics
From realistic analogue to virtual reality
Mick van der Wegen m.vanderwegen@un-ihe.org
Associate Professor Estuarine Dynamics
and
Senior Researcher at Deltares

## Slide 6: Learning objectives
At the end of the course you can
qualify estuaries based on their hydrodynamic and sediment driven forcing
distinguish characteristic morphodynamic adaptation time scales in estuaries
assess the importance of tidal flats
explain the Escoffier curve for inlets

## Slide 7: Activities
3 periods - lectures
  Introduction classification, equilibrium?
  Inlet systems
  From realistic analogue to virtual reality
    Schematized inlet and tidal basin
    Forcing geometry :Western Scheldt
    150 year hindcast in Western Scheldt : model skill
    150 year hindcast and 100 year forecast in San Pablo Bay : model confidence, do we trust our model?
Homework – reading stuff – prepare ppt
1 period, you present in small groups!

## Slide 8: Assessment
Active attendance
Participation in group discussions/presentation

## Slide 9: Estuarine morphodynamics The study of forms where a river meets the sea

## Slide 10
Loire estuary, France

## Slide 11
Mersey and Dee estuary, UK

## Slide 12
Benin

## Slide 13
Yangtze estuary, China PR

## Slide 14
Kalimantan, Indonesia

## Slide 15
Time
Space
Morphological Time and Length Scales
Morphological
features

## Slide 16: sand mud
Land van Saeftinghe, Netherlands

## Slide 17: Morphological classification based on
Features
Sediment
Forcing
Vegetation/ecology

## Slide 18: Time

## Slide 20: Equilibrium?
Time scale
Spatial scale
Dynamic equilibrium
Asymptotic equilibrium

## Slide 21: Empirical relationships
Jarret (1976, based on O’Brien (1931)) for an open inlet:
where
A = Cross sectional area below MSL
P = Tidal prism
Tidal influence
Tidal difference
P
A

## Slide 22: Empirical relationships
Eijssink :
where
Vc = Channel volume
below MSL
P = Tidal prism

## Slide 23: Would it be possible to derive empirical relationships with a process-based model?

## Slide 25: Model formulation
Shallow water equations

## Slide 26: Model formulation
Engelund Hansen transport formula
Bed level update

## Slide 27: Morphodynamic update
Delft3D online
  (morphodynamic update every hydrodynamic timestep, morphological factor of 200)

## Slide 28: Bed slope effects
Magnitude acc. to Bagnold (1966)
Direction acc. to Ikeda (1982, 1988)
S’
Sn
Stotal
S

## Slide 29: Model configuration

## Slide 30: Model configuration
Bank (dry cell) erosion; calculated erosion of wet cell is assigned to eroding level of adjacent dry cell
water level
dry
wet
dry
wet
dry
wet
wet

## Slide 32: Width averaged longitudinal profile for fixed banks and erodable banks

## Slide 33
Tidal amplitude for fixed banks and erodable banks

## Slide 34
Maximum ebb and flood velocities for fixed banks and erodable banks
* Initial
+ 200 years
800 years
3200 years

## Slide 35: Ebb and flood duration for fixed banks and erodable banks
* Initial
+ 200 years
800 years
3200 years

## Slide 36: Development along equilibrium
Development along equilibrium; two timescales:
Pattern formation (first 20 years) with deltaic bed forms and alternating bar pattern- determined by local and constant (during development time) hydrodynamics
Width averaged profile development (centuries)-determined by interaction between tide and bed

## Slide 37: What is the basin aiming for?

## Slide 38: Energy dissipation formulation (Rodriquez-Iturbe (1992) )
Formulation based on optimal drainage networks
Energy dissipation = function (shear stress, sediment transport):
or in 2D numerical modeling terms

## Slide 39
Energy dissipation (Ediss/m^2/s) for fixed banks

## Slide 40
Energy dissipation (Ediss/m^2/s) for erodible banks

## Slide 42: How do model results compare to empirical relationships?
Jarret (1976, based on O’Brien (1931)) for an open inlet:
where
A = Cross sectional area below MSL
P = Tidal prism

## Slide 43
Fixed banks
Erodible banks
initial
3200 years
800 years
200 years
Jarrett jettied inlet
Jarrett free inlet

## Slide 44: Observations
Model results fit nicely to empirical relationship
Although there is continuous and ongoing development
PA relationship is constant along the basin
PA relationship for a jettied inlet (or: fixed banks basin) is steeper than for a ‘free’ inlet (or: basin with erodable banks)
What is the reason for this? Can we explain the PA relationship?

## Slide 45: Concluding remarks
Evolution leads to “equilibrium” on short time scales;
Evolution leads to ongoing but decreasing dynamics on (very) long time scales;
Indicators for equilibrium by
  Fit to empirical relationship
  Equal ebb and flood duration
  More uniform distribution of velocities and energy dissipation along the basin
  decreasing energy dissipation and dissipation rate

## Slide 47: Exercise – intertidal area
Prepare a 15 minute lecture for your fellow students on
  Nature-based flood defenses in estuaries - How do these work?
  Sea level rise and estuaries- What happens?
  Ecosystems on intertidal flats – What happens?
High quality! (of course….)
  Fundamentals
  Case studies
  3 cited journal papers
  Movies
  others?
Will be followed by 5 minute critical questions from fellow students

## Slide 49: Reproduction of the Western Scheldt bathymetry by means of a process-based, morphodynamic model
Mick van der Wegen and Dano Roelvink
What are the main driving forces that determine the morphological patterns in a tidal embayment?
or:

## Slide 50: Question :
What is the impact of the geometry on the location of the patterns?
hydrodynamics
geometry
bathymetry

## Slide 52
50 km
No river discharge
Only M2 tidal forcing

## Slide 55
1998 bathymetry
Flattened bathymetry
After 15 years
After 30 years
After 200 years

## Slide 56: Variations:
Tidal Forcing M2, M4, M6
Transport formulation Engelund Hansen, Van Rijn
Bed slope parameter
2D, 3D
Inclusion/exclusion :
  Dredging and dumping actvities
  River discharge (500 m3/s)
  Non-erodible substrate
Sediment grain size

## Slide 57
measured 1998
EH-2D

## Slide 58
measured 1998
EH-3D-M2

## Slide 59
measured 1998
EH-3D-nel

## Slide 60: Mean depth
Exporting basin:
About 1m deepening over 200 years
~100 Mm3/200 years
~500,000 m3/year

## Slide 61: Hypsometry after 200 years

## Slide 62: Brier Skill Score
Δvol - volumetric change compared to the initial flat bed, (m3)
mod - modeled quantity,
meas - measured quantity
=1 is perfect model
<0 is worse than a flat bed

## Slide 63
1
0.75
0.75
0.76
0.83
BSS

## Slide 64: Brier Skill Score
1= perfect

## Slide 65: What determines the BSS?
Amplitude (α)
(size of the patterns)
Phase (β)
(location)
Mean level (γ)
Pattern formation
Pattern formation
Longitudinal profile
(Sutherland et al. 2004)

## Slide 66
Phasing
Amplitude and Phasing
Mean level

## Slide 67: Conclusions
Modeling approach reproduces realistic and characteristic patterns in the Western Scheldt tidal basin.
Major tidal forcing shows significant skill in reproducing the bathymetry, even for variations in model parameter settings.
Model performance varies over 200 years due to continuous pattern formation and deepening of the basin

## Slide 69
Long-term performance of morphological models in estuaries
Virtual reality?
Gerard Dam (Svasek Hydraulics/UNESCO-IHE)
Mick van der Wegen (UNESCO-IHE, Deltares)
Dano Roelvink (UNESCO-IHE, Deltares)

## Slide 70: ....the weather forecast for the next days....
(www.buienradar.nl)

## Slide 71: How do process-based models perform?
Morphodynamic activity
Time
Measured reality

## Slide 73: Morphological process-based model:
FINEL2d model (www.finel2d.com ):
2DH simulation finite elements method;
Only tidal forcing;
Engelund-Hansen sediment transport formula
1 fraction of sand
Roughness constant in time and space
MORFAC: 24.75
Non-erodable layer
Parameterisation of spiral flow
Water motion calibrated

## Slide 74: Computational grid

## Slide 75: Computational grid

## Slide 76: Computational grid

## Slide 77: 110 years hindcast period 1860 - 1970
Bathymetric recordings in:
1860- initial bathymetry
1878
1890
1905
1931
After 1955 every 2 years till 1970

## Slide 78: Erosion/sedimentation 1860-1878 (18 years)

## Slide 79
Erosion/sedimentation 1860-1890 (30 years)

## Slide 80: Erosion/sedimentation 1860-1905 (45 years)

## Slide 81: Erosion/sedimentation 1860-1831 (71 years)

## Slide 82
Erosion/sedimentation 1860-1955 (95 years)

## Slide 83
Erosion/sedimentation 1860-1960 (100 years)

## Slide 84
Erosion/sedimentation 1860-1970 (110 years)

## Slide 85: Brier-skill score (Sutherland et al., 2004)
Where:
Y=Bed level prediction at time T
X=Bed level observation at time T
B=Bed level at t=0
And the <> denote the arithmetic mean.
Rating (van Rijn et al., 2003):
<0 : Bad
0– 0.3 : Poor
0.3- 0.6 : Reasonable/fair
0.6- 0.8 : Good
0.8- 1.0 : Perfect

## Slide 86: BSS 1860 – 1970; entire Western Scheldt

## Slide 87: Error and signal 1860 – 1970

## Slide 88: BSS: 3 hindcast periods

## Slide 89: Error and signal; 3 hindcast periods
30 years spin-up

## Slide 90: How do process-based models perform?
Morphodynamic activity
Time
Measured reality
Modeled reality

## Slide 92
Van der Wegen and Roelvink, Geomorphology, 2012

## Slide 93: Concluding remarks
Model performs well in confined systems
Performance of is weak in the first decades, but increases significantly on the longer run
  Weak performance due to limited process description and initial data settings
  Strong performance due to impact of geometry (outline and shape)
Long-term (> decades) predictions seem more valuable than decadal predictions
How to decrease morphodynamic spin-up time?
Importance of sand and mud?

## Slide 94: Net annual sediment transport (sediment balance study)
Untill recently transports believed to be all sand

## Slide 95: Net annual sediment transport (sediment balance study)
Sand
Mud
Annual sediment transport (1994-2010)
For long term morphological changes: also mud!

## Slide 96: 725 year calculation of Western Scheldt from flat bed
-Sand versus Sand-mud model
Sand-mud: Including effect of cohesive behaviour of bed above 30% mud in top layer of bed
(making it harder to erode than pure sand bed)
-Start with fully sandy bed
-Mud concentration at sea boundary

## Slide 99: Hindcast 1860 - 1970
-Sand versus Sand & Mud model
-Start in 1860 fully sandy bed
-Mud concentration at sea boundary

## Slide 100: Hindcast 1860-1970: zand versus zand + slib
Zand
Zand + slib

## Slide 101: Future research: Meer fysica: SLIB!!!!!!!!
MODEL: Sand
MODEL: Sand + mud
Observation
Erosion/sedimentation 1860-1970

## Slide 103
https://beeldbank.rws.nl, Rijkswaterstaat

## Slide 105
Benin

## Slide 107
Energy dissipation (Ediss/m^2/s) for fixed banks

## Slide 109
Erosion/sedimentation 1860-1970 (110 years)

## Slide 110: BSS 1860 – 1970; entire Western Scheldt

## Slide 111: Error and signal 1860 – 1970

## Slide 113
Source: Beachapedia
Source: www.e-education.psu.edu, D. Fitzgerald
Source: Dissanayake, 2015

## Slide 114: What happens in an inlet?
Are inlets stable?
What causes equilibrium?
What are important processes?

## Slide 116
Tidal movement
Short basin

## Slide 117
Tidal movement
Short basin

## Slide 118: Model formulation
Shallow water equations:
Mass balance:
L
B
h0
hb, Ab
Q

## Slide 119: Model formulation
Shallow water equations: Momentum balance
Consider only x-momentum
Integrate over inlet width (B)
Neglect Reynold shear stresses

## Slide 120
Integrate over inlet length (L)
and depth (h)
Neglect advection:
with
L
B
h0
hb

## Slide 121
Assuming
The friction term can be linearized by
So that momentum equation
becomes
with

## Slide 122
Combining mass and momentum equations
and
Leads to the 2nd order differential equation
That describes a damped spring-mass system
with

## Slide 123
Introducing the natural or Helmholtz frequency
the solution to the equation
with
is of the form
and

## Slide 124
From mass balance equation
follows that the amplitude of the discharge in the inlet can be given by:
and
whereas the amplitude of the velocity can be approximated by
given h0, Ab, Ac, L, ω, cf

## Slide 125: What does the solution look like for a given basin area and tidal forcing? (Escoffier curve)

## Slide 126: What is the morphodynamic response ?

## Slide 127: Can this be reproduced by a process-based morphodynamic model ?

## Slide 128: Yes! (at least for large cross-sections):
Analytical solution
PB-Model solution - velocity
PB-Model solution - discharge

## Slide 129: Equilibrium by
Morphodynamic evolution leads to shear stresses lower than critical shear stress for sediment movement.
  No sediment transport seems unrealistic
…
…

## Slide 130: Equilibrium in a real inlet: the influence of waves
The amount of littoral drift (M) that enters the inlet during flood is equal to the amount of sediment exported during ebb (Sebb).
M=Sebb

## Slide 131
Littoral drift
Waves
Tidal movement

## Slide 132
Littoral drift
Waves
Tidal movement
FLOOD
Deposition after flood

## Slide 133
Littoral drift
Waves
Tidal movement
EBB
Deposition after ebb

## Slide 134
40 m
Deep basin
Littoral drift

## Slide 135
Equilibrium depends on ratio of (littoral drift) sediment source to tidal transport capacity

## Slide 136: Tide only Tide and littoral drift
Jarrett (1976) - free
Jarrett (1976) - jettied
A=CPn

## Slide 137: Tide only Tide and littoral drift
Velocity, m/s
Analytical solution
Discharge, m^3/s
Analytical solution
Cross sectional area, m^2
Cross sectional area, m^2

## Slide 138: Equilibrium in inlets
flood
ebb
Flood : erosion
Ebb : erosion
Littoral drift
Flood : accretion
Ebb : erosion

## Slide 139: Equilibrium by
Morphodynamic evolution leads to shear stresses lower than critical shear stress for sediment movement
  No sediment transport seems unrealistic
Littoral drift
  Very small amount compared to tide driven transport
…

## Slide 140
40 m
40 m
Deep basin
Shallow basin

## Slide 141: Comparison deep basin to shallow basin
Shallow basin
Deep basin

## Slide 142
Shallow basin leads to smaller spatial transport gradients; slower development
Equilibrium needs zero spatial gradients in tide residual sediment transports

## Slide 143
Fixed banks
Erodable banks
initial
3200 years
800 years
200 years
Jarrett jettied inlet
Jarrett free inlet

## Slide 144: Equilibrium by
Morphodynamic evolution leads to shear stresses lower than critical shear stress for sediment movement
  No sediment transport seems unrealistic
Littoral drift
  Very small amount compared to tide driven transport
Adjacent channel-shoal system: very low spatial gradients in tide residual sediment transports

## Slide 146
Littoral drift
Waves
Tidal movement

## Slide 147: What is the morphodynamic response ?

## Slide 148: Equilibrium by
Morphodynamic evolution leads to shear stresses lower than critical shear stress for sediment movement
  No sediment transport seems unrealistic
Littoral drift
  Very small amount compared to tide driven transport
Adjacent channel-shoal system: very low spatial gradients in tide residual sediment transports

## Slide 149: Learning objectives
At the end of the course you can
qualify estuaries based on their hydrodynamic and sediment driven forcing
distinguish characteristic morphodynamic adaptation time scales in estuaries
assess the importance of tidal flats
explain the Escoffier curve for inlets

## Slide 150: Today
Sea level rise in tidal basins
Schematized case
Case study, California US

## Slide 152: Imposing sea level rise:

## Slide 154: Cumulative sediment transport
Straight lines : no sea level rise
Dotted lines : with sea level rise
What is causing the shift from sediment export to import?

## Slide 155
Width averaged depth

## Slide 156: Intertidal area
No SLR
SLR

## Slide 157: Tidal asymmetry

## Slide 158: Tidal asymmetry
Q (m3/s)
t (s)
Flood duration
Ebb duration
M2
M4
M2+M4

## Slide 159: Tidal asymmetry
t (s)
Flood duration
Ebb duration
M2
M4
M2+M4
Q (m3/s)

## Slide 160: Sediment transport (~ U3-5)
t (s)
Generation of ‘overtide’ (super harmonic component), M4, results in tidal asymmetry and flood dominance (this case).
Q (m3/s)

## Slide 161: Generation of overtides (M4, M6, M12, etc.)
Due to interaction between hydrodynamics and bathymetry:
friction
presence of intertidal area
water depth influence on wave propagation
(and other factors)

## Slide 162: Tidal asymmetry: water depth influence on wave propagation
h (m)
x (m)
x (m)
h (m)
Shorter flood duration and higher flood velocities
Larger asymmetry for shallower water;
Flood

## Slide 163: Tidal asymmetry: influence of intertidal area

## Slide 164: Tidal asymmetry: influence of intertidal area
h (m)
x (m)
x (m)
h (m)
Longer flood duration and lower flood velocities
Larger asymmetry for more intertidal area;
Flood

## Slide 165: Tidal symmetry (equilibrium) by counteracting influence of
- presence of intertidal area
water depth influence on wave propagation
What happens when intertidal area disappears?

## Slide 166: Tidal asymmetry

## Slide 167: Different forcing: intertidal area
0.85 m 1.75m 3.5m

## Slide 168: Different forcing: sediment transport
0.85 m 1.75m 3.5m

## Slide 169: Different forcing: tidal asymmetry
0.85 m 1.75m 3.5m

## Slide 170: Summary
Sea level rise induces sediment import into tidal embayments;
Shift from export to import does not provide enough sediment to the shoals to maintain intertidal area;
Drowning of intertidal area contributes to tidal asymmetry and sediment import.
Intertidal area is more vulnerable to sea level rise for shallow, young tidal basins;

## Slide 172
https://beeldbank.rws.nl, Rijkswaterstaat

## Slide 175
Energy dissipation (Ediss/m^2/s) for fixed banks

## Slide 176
Erosion/sedimentation 1860-1970 (110 years)

## Slide 177: BSS 1860 – 1970; entire Western Scheldt

## Slide 179
Source: Beachapedia
Source: www.e-education.psu.edu, D. Fitzgerald
Source: Dissanayake, 2015

## Slide 180
Littoral drift
Waves
Tidal movement

## Slide 181: Equililbrium

## Slide 182: Equilibrium by
Morphodynamic evolution leads to shear stresses lower than critical shear stress for sediment movement
  No sediment transport seems unrealistic
Littoral drift
  Very small amount compared to tide driven transport
Adjacent channel-shoal system: very low spatial gradients in tide residual sediment transports

## Slide 183: Imposing sea level rise:

## Slide 184: Different forcing: intertidal area
0.85 m 1.75m 3.5m

## Slide 185: Tidal asymmetry
Q (m3/s)
t (s)
Flood duration
Ebb duration
M2
M4
M2+M4

## Slide 186: Hindcasting bathymetric change in San Pablo Bay A step towards assessing likely geomorphic change in response to climate change
Mick van der Wegen1, Dano Roelvink1 and Bruce E. Jaffe2
1 UNESCO-IHE
2 U.S. Geological Survey

## Slide 187
500 km
California
San Francisco
Los Angeles
Sacramento
Courtesy J. Cloern
California

## Slide 188
Delta
2
San Francisco Bay
Sacramento R.
San Joaquin R.
Sierra Nevada
Pacific Ocean
Courtesy J. Cloern

## Slide 189: Hydraulic mining

## Slide 190
San Francisco Estuary
in the 1980s
Area: ~1200 km2
Average depth: 7 m
Median depth: 3 - 4 m
Deepest point: ~120 m
(Golden Gate)
San Pablo Bay
Central Bay
Suisun Bay
South Bay
Jaffe 2009
Notes: Point out color scheme
Point out 10 km scale bar
Point out sub-embayment names
1980s is the most recent complete bay bathymetry data set
Average depth increased by deep Central Bay

## Slide 192: The Data
Image obtained from NOAA photo library (www.photolib.noaa.gov)
Notes: Old data is good, craftsmen

## Slide 193: Three characteristic periods
Excess sediment supply due to hydraulic mining about 150 years ago – measured deposition.
Dramatic decrease in sediment supply after stop in hydraulic mining and dam construction in the last century – measured erosion.
Climate change will further perturb the morphodynamics as sea level rises and the river discharge regimes are altered by warming and precipitation changes – further erosion?

## Slide 194: Deposition in San Pablo Bay 1856 to 1887
Average net deposition was
~ 8 million m3/yr
Jaffe et al. (2007)

## Slide 195: Erosion in San Pablo Bay 1951 to 1983
Average net
erosion was
~ 0.8 million m3/yr
Jaffe et al. (2007)
Jaffe et al. (2007)

## Slide 196: Aim of the study
To hindcast bathymetric changes in San Pablo Bay with a process-based morphodynamic model
To compare model results to decadal measured bathymetric development
With the final aim (not this study) to assess impacts of climate change.

## Slide 197: Subquestion 1:
Can a process-based, 3D, numerical model reproduce historic sedimentation volumes and patterns?

## Slide 198: Delft 3D
Process-based 3D numerical model
Shallow water equations
Multiple transport formulations
Multiple sediment fractions
Bed slope effects
Bed level update every time step
Waves, density currents

## Slide 199: Boundary conditions

## Slide 200: Schematization by applying only M2, M4, K1 and O1 at the boundaries

## Slide 201
  Sediment supply via Qs = α Qr β (historic proxy by Ganju et al (2008))

## Slide 202: Model schematization
Wind diurnal with 7 m/s around noon
  6 months from the west
  5 months from south east
Sediment transport formulae
  Van Rijn for sand, 3 fractions
  Krone/Partheniades for mud, 5 fractions

## Slide 203: Unknown parameters
Sand fractions 9
Mud fractions 20
Wind 4
Flow 10
Wave 10
Total 53 !!
Some physically unknown (not measured)
Some introduced by schematization (time-saving)

## Slide 204: Subquestion 2
To analyze governing conditions and processes that cause decadal timescale channel narrowing in San Pablo Bay by means of a 3D process-based model (Delft3D).

## Slide 205: Van der Wegen et al., OD and JGR, 2011
Can a process-based model (like Delft3D) reproduce decadal morphodynamics?
Measured
Modeled
1856-1887 1951-1983 1983-2013

## Slide 206: Subquestion:
How sensitive are model results to
- model parameter variation and
- flow schematization?

## Slide 207
1856-1887 1951-1983 1983-2013
volume change per year

## Slide 208: Brier Skill Score (1=perfect)

## Slide 209
1856-1887 1951-1983
BSS

## Slide 210: Van der Wegen et al., submitted
Seasonal fluctuations (modeled)
1856-1887
1951-1983
high river flow low river flow total

## Slide 211: SLR schematization
MSL
0.2 m
wet dry
1983 2013 2046 2079 2113
Water level, m
Time, year
0.5 m
1 m

## Slide 212
2013-2046 2046-2079 2079-2113
2013-2046 2046-2079 2079-2113
With sea level rise
Constant mean sea level
+ 0.2 m + 0.5 m + 1 m

## Slide 213: erosion and sedimentation 2013-2113 No SLR SLR
-2 m
2 m

## Slide 214: Large historic variation in intertidal area
Volume change, Mm3
Intertidal area, Mm2
Time, year
No SLR
SLR
Model validated
Unvalidated forecast

## Slide 215: Intertidal area drops from 17% to 2% in 100 years with SLR, despite net deposition
Volume change, Mm3
Intertidal area, Mm2
Time, year
No SLR
SLR

## Slide 216: Conclusions
We modeled 250 years of morphodynamic development in San Pablo Bay, California
150 hindcast validation provides confidence in 100 year forecast without (and with) sea level rise
Intertidal area will slowly decay from 17% to 2% within a century under SLR scenario of 1 m/century.
The research is part of the US Geological Survey CASCaDE climate change project (CASCaDE). The authors acknowledge the US Geological Survey Priority Ecosystem Studies and CALFED for making this research financially possible.

## Slide 217: Learning objectives
At the end of the course you can
qualify estuaries based on their hydrodynamic and sediment driven forcing
distinguish characteristic morphodynamic adaptation time scales in estuaries
assess the importance of tidal flats
explain the Escoffier curve for inlets

## Slide 219: What is the model performance in terms of accuracy and skill?
How much precent of the modeled volume is accurate and has skill?

## Slide 220
measured μ modeled σ
(ensemble averaged)
μ/σ > 3
μ/σ BSS BSS > 0.5

## Slide 221: Forecast
μ modeled σ μ/σ
(ensemble averaged)

## Slide 222: Confidence index

## Slide 223: Model performance indicator (MPI) combination of uncertainty and skill
indicator | criterion | 1856-1887 | 1951-1983 | 1983-2013
Accuracy | CI>0.3 | 90% | 68% | 60%
Skill | BSS>0.5 | 57% | 19% | 
MPI | CI>0.3 BSS>0.5 | 53% | 9% | 
xx % of the modeled erosion and sedimentation volume fulfils the criterion

## Slide 224
1856-1887 period
1951-1983 period
1983-2013 period
Accuracy performance
Skill performance
Volume / Total volume

## Slide 225: Accuracy performance

## Slide 226: Concluding remarks
Model performance should be expressed in terms of skill and uncertainty

## Slide 227: Learning objectives
At the end of the course you can
specify estuaries based on their hydrodynamic and sediment driven forcing
describe characteristic morphodynamic adaptation time scales in estuaries
indicate (im-) possibilities of modeling efforts addressing estuarine morphodynamic developments based on scientific literature

## Slide 228: Fin

## Slide 229: Van der Wegen et al., submitted
Seasonal fluctuations (modeled)
1856-1887
1951-1983
high river flow low river flow total

## Slide 230: What are governing tidal conditions?
●

## Slide 231: - 60% of the slope deposition occurs during flooding of the shoals; - 75 % of the slope erosion occurs during ebbing of the shoals;

## Slide 232: Why does the channel narrow?
Under conditions of high Suspended Sediment Concentration (SSC) due to
River supply during the wet season
Wind wave action on the shoals
Intertidal morphodynamic development is significantly larger than tide-residual deposition and erosion patterns.
Flooding of the shoals is an important but not the only condition in which deposition takes place.

## Slide 233
2013-2046 2046-2067 2067-2100
2013-2046 2046-2067 2067-2100
With sea level rise
Constant mean sea level
+ 0.2 m + 0.5 m + 1 m

## Slide 234: Current conditions Sea level rise (1 m/100yr)

## Slide 235: Summary
Van der Wegen et al., OD and JGR, 2011
Measured
Modeled
1856-1887 1951-1983 1983-2013

## Slide 237
From the 1850s-1980s
Circular bays near the center of the Estuary bays (San Pablo and Central) had net deposition
Elongate bays at ends of estuary (Suisun and South) had net erosion
From 1950s-1980s
All bays were erosional
Net
Net
Notes: Summary of behavior of bays.

## Slide 238
Outline
The Estuary in the past 150 years
Sediment delivery control on net sedimentation and tidal flat change
Notes: Example of an application of this approach to learn morphodynamic behavior.

## Slide 239
Net sedimentation responded to changes
in river
sediment supply to San Pablo Bay
Jaffe et al. 2007
Notes: Trends in net sedimentation reflected the decrease in sediment supply. The system became erosional when sediment supply decreased below about 4 or 5 Mcm/yr.

## Slide 240
Tidal flats of the estuary have changed
1850s
1890s
1920s
1950s
1980s
Notes: The light brown are the tidal flats.
Tidal flat extent and width changed over time.

## Slide 241
San Pablo Bay
Central Bay
Suisun Bay
South Bay
1850s
1890s
1920s
1950s
1980s
0
20
40
60
80
100
km2
0
20
40
60
80
100
km2
0
20
40
60
80
100
km2
0
20
40
60
80
100
km2
Tidal flat area decrease >50%
Notes: Tidal flat area varied over time and by bay.

## Slide 242
Box Model for San Pablo Bay
Jaffe et al. 2007
Notes: We developed a box model to explore the importance of the terms in the sediment budget.
This is a busy slide. Details are presented in a 2007 publication.
The next slide looks at how major terms in the sediment budget changed over time.

## Slide 243: Conclusions
Process-based, 3D, numerical model can reproduce decadal sedimentation volumes and patterns fairly well
The depositional period shows better results than the erosion period
Erosion mechanisms depend to a high degree on limited data on bed composition
Model results remain quite consistent by model parameter variation within reasonable limits
This suggests that the geometry and bathymetry play a major role in the morphodynamic development of San Pablo Bay.

## Slide 244: Fin

## Slide 245: Fin

## Slide 246: Summary
Time and length scales from pattern formation (~ decades, basin width) to basin evolution (~millennia, basin length);
Basin aims for less energy dissipation (sediment transports or morphodynamic development) at continuously smaller rate;
The geometry of the basin plays a significant role in the allocation of channel shoal patterns;
Major forcing and sediment availability in a given geometry give recognizable patterns;
Best-guess model parameter settings lead to realistic decadal morphodynamic development even in complex environments;

## Slide 247: Summary

## Slide 249
Depth, m
0
-20
-10
1856-1887

## Slide 250: Sediment volume change in San Pablo Bay from 1856 to 1887
Average net sediment deposition was
~ 8 million m3/yr
Current conditions show erosion of
~ 0.8 million m3/yr
Jaffe et al. (2007)

## Slide 251
sea
basin
island
ebb delta
channel
flats

## Slide 252: Empirical relationships
Jarret (1976, based on O’Brien (1931)) for an open inlet:
where
Ac = Cross sectional area below MSL, m2
P = Tidal prism, m3

## Slide 253: Empirical relationships

## Slide 254: Vs/Vc versus a/h for fixed banks and erodable banks

## Slide 255
Box Model for San Pablo Bay
Jaffe et al. 2007
River sediment supply decreased over time
Notes: River supply estimates from studies, simplified from an earlier slide.

## Slide 256
Box Model for San Pablo Bay
Jaffe et al. 2007
deposition
+
up-estuary
storage
=
river sediment supply
Notes: Deposiiton and upstream storage, two terms we have a fairly good handle on, do not equal the river sediment supply.

## Slide 257
Box Model for San Pablo Bay
Jaffe et al. 2007
erosional loss
+
bypassing
+
deposition
+
up-estuary
storage
=
river
sediment supply
Sediment Bypassing
~ 5 Mcm/yr
Erosional Loss
~ 3 Mcm/yr
Notes: Point out scale of 10 km
Big changes (10+ m of change at channel margins)
Patterns of channel migration (Suisun Bay) and channel narrowing (San Pablo Bay)
Changes mainly not anthropogenic
Each bay behaves somewhat differently

## Slide 258
Mudflats widened where sediment was abundant
Jaffe et al. 2007
Notes: The relation erosion or deposition of the shallows and narrowing or growth of the tidals is brought out by analyzing sub-regions of the Bay.

## Slide 259
Intertidal mudflat area responded to changes
in sediment supply to San Pablo Bay
Jaffe et al. 2007
Notes: Tidal flat area increased when there was a large supply of sediment and decreased when sediment supply was less than about 5 Mcm/yr.