## Slide 1: Water supply from NBS for irrigation & cropping
Application systems

## Slide 2: Definitions

## Slide 3: Application system: what is it?
Definion: The system (technology, practice or construction) that distribute the water coming from the system, to the plant.1
In practice: Examples
Drip irrigation, sprinklers, spray tubes, etc.
Manual application with a hose or a watering can
Furrows digged in the field
Each type of system has a specific efficiency.
1. Source: Merriam-Webster dictionnary, 2021.

## Slide 4: Efficiency: what is it?
Definition: it is the percentage of water that enters the application system and will actually reach the plant.
Even in a perfect condition, an application system is never 100% efficient, there are losses:
Losses in the air: by evaporation or splashing away from the plant
Losses in the soil: water infiltrates the deeper layers of the soil
Water distribution methods
[Leakage if the system is damaged]
=> Losses in the application need to be accounted for when calculating the required pump yield otherwise less water than expected will reach the plant.

## Slide 5: Common types of application systems

## Slide 6: Drip irrigation
Efficiency: Around 90%  Very efficient
Application pressure: 1 to 5 m  Works with very low pressure, but often requires a tank
Design & installation: difficult
Price: expensive
Lifespan: depends on quality/type
of materials.
Labour: very low

## Slide 7: Drip irrigation layout
Sector (can be irrigated independently from the others)

## Slide 8
System being installed
Drip irrigation system
Connections between the sectors
Open valve
Main conveyance pipe
Closed valve

## Slide 9: Furrows
Efficiency: Around 30-40%  Not efficient (water losses in the soil)
Application pressure: 1 m  Works with low pressure
Design & installation: easy
Price: cheap
Labour: moderated
Because of the very high water losses, furrows are NOT recommended with:
  Solar pumps
  Pumps of a low capacity
  When water availability at the water source is limited

## Slide 10: Watering can
Water efficiency: Around 90%  Efficient
Application pressure: ~1 m  Works with low pressure
Design & installation: easy  Watering cans can be filled from a basin fed by the pump.
Price: cheap (labour costs)
Labour: intensive
Irrigation with watering cans is very time consuming.

## Slide 11: Sprinklers
Efficiency: Around 60%  Low efficiency
Application pressure: 15 m  Works with very high pressure
Design & installation: easy
Price: moderated
Labour: low

## Slide 12: Spray tubes
Efficiency: Around 80%  Efficient
Application pressure: 5 to 10 m  Works with relatively low pressure
Design & installation: moderated
Price: Moderated
Labour: low

## Slide 13: Spray tube layout
Sector (can be irrigated independently from the others)

## Slide 14
Sector

## Slide 15: Others
Spray hose
Low cost basins
Californian System
Mini Pivot