## Slide 1
Stef Smits, IRC
Training of trainers 4: Multiple-Use Services: combining domestic water supply and irrigation systems smartly
MUS as an approach

## Slide 2: Introduction
Given the various potential entry points, and the many variables involved, MUS requires a structured approach
Programming approach, from assessment via planning and implementation to monitoring
Accompanied by interventions to create an enabling environment for MUS
Brought together in a set of guidelines

## Slide 3
1. Introducing multiple-use water services to water users and service providers
2. Situational assessment
3. Visioning and strategic planning
5. Implementation of MUS interventions
6. Support to continuous service provision
4. Fitting the financial framework
A: Evidence-based advocacy on potential and barriers of MUS
B: Capacity development for an enabling environment for MUS
Enabling environment
Service provision

## Slide 4
1. Introducing multiple-use water services to water users and service providers
2. Situational assessment
3. Visioning and strategic planning
5. Implementation of MUS interventions
6. Support to continuous service provision
4. Fitting the financial framework
A: Evidence-based advocacy on potential and barriers of MUS
B: Capacity development for an enabling environment for MUS

## Slide 5: Set-up of the guidelines
1. Introducing multiple- use water services to water users and service providers
2. Situational assessment
3. Visioning and strategic planning
5. Implementation of MUS interventions
6. Support to continuous service provision
4. Fitting the financial framework
A: Evidence-based advocacy on potential and barriers of MUS
B: Capacity development at intermediate and national level
Part 1: MUS concepts and entry points
Part 2: Guidelines for planning and provision of MUS
Part 3: Guidelines for the development of an enabling environment for MUS
Part 4: tools
For each tool:
Objective
Method
Tips and tricks
Based on
Further reading
For each phase:
Objective
Activities
Tools

## Slide 6
1. Introducing multiple- use water services to water users and service providers
2. Situational assessment
3. Visioning and strategic planning
5. Implementation of MUS interventions
6. Support to continuous service provision
4. Fitting the financial framework
A: Evidence-based advocacy on potential and barriers of MUS
B: Capacity development at intermediate and national level
Tool 1- Community meeting to raise interest in multiple use water services
Tool 2 - Getting in-depth information and lots of good ideas: focus group discussion
Tool 3 - Water user categorisation: Livelihood groups and wealth ranking
Tool 4 - Identification of water services and users
Tool 5 - Rapid Appraisal Process for MUS system
Tool 6 - Identification of user representation
Tool 2 - Getting in-depth information and lots of good ideas: focus group discussion
Tool 3 - Water user categorisation: Livelihood groups and wealth ranking
Tool 4 - Identification of users of multiple water use services
Tool 5 - Rapid Appraisal Process for MUS system
Tool 6 - Identification of user representation
Tool 7 – Community mapping
Tool 8 – Seeing is also learning: village walk
Tool 9 - RIDA: Analysis of water resources, infrastructure, demand and access
Tool 10 - Village water resources assessment
Tool 11 - Assessing demand for water for different uses
Tool 12 - Household questionnaire on water resources, infrastructure, water demand and use
Tool 13 - Water quantity measurements from water resources and infrastructure
Tool 14 – Surveying water resources and infrastructure
Tool 15 - Identification of water access constraints
Tool 16 – Data collection on Life-Cycle Costs
Tool 17 - Estimating the benefits of services
Tool 18 - MUS Visioning
Tool 19 – Strategy development
Tool 20 - Selection of technologies for multiple uses
Tool 16 - Data collection on Life-Cycle Costs
Tool 17 – Estimating the benefits of services
Tool 21 - Training of (community level) service providers
Tool 21 - Training of (community level) service providers
Tool 22 - Monitoring
Tool 4 - Identification of users of multiple water use services
Tool 16 – Data collection on Life-Cycle Costs
Tool 17 - Estimating the benefits of services
Tool 23 - Actor and task analysis
Tool 24 - Set-up and facilitation of a learning alliance
Part 2
Part 3
Part 4: Tools

## Slide 7
Objective
to make water service providers and users aware of the potential and limitations of multiple-use water services in a certain context.
Activities
Getting to understand the context
Raising interest on MUS at user and service provider level
Setting expectations and conditions
1. Introducing multiple-use water services to water users and service providers

## Slide 8
Tools:
Tool 1- Community meeting to raise interest in multiple use water services
Tool 2 - Getting in-depth information and lots of good ideas: focus group discussion
Tool 3 - Water user categorisation: Livelihood groups and wealth ranking
Tool 4 - Identification of water services and users
Tool 5 - Rapid Appraisal Process for MUS system
Tool 6 - Identification of user representation
1. Introducing multiple-use water services to water users and service providers

## Slide 9
Objective
to get a good insight into the current and projected future situation of water resources, water infrastructure, water demand and water use of different social and economic groups, at household, community, system and / or basin level.
Activities
Assessment of water resources
Assessment of water infrastructure
Assessment of optimal water demand
Assessment of actual water use and barriers to accessing water services
Analysis of water Resources, Infrastructure, Demand and Access
Data storage and presentation
2. Situational assessment
Water resources
Infrastructure (hard and software)
Water services (quantity, quality, accessibility, reliability)
Water use (quantity, quality, accessibility, reliability)

## Slide 10
Tools
Tool 2 - Getting in-depth information and lots of good ideas: focus group discussion
Tool 3 - Water user categorisation: Livelihood groups and wealth ranking
Tool 4 - Identification of users of multiple water use services
Tool 5 - Rapid Appraisal Process for MUS system
Tool 6 - Identification of user representation
Tool 7 - Community mapping
Tool 8 - Seeing is also learning: village walk
Tool 9 - RIDA: Analysis of water resources, infrastructure, demand and access
Tool 10 - Village water resources assessment
Tool 11 - Assessing demand for water for different uses
Tool 12 - Household questionnaire on water resources, infrastructure, water demand and use
Tool 13 - Water quantity measurements from water resources and infrastructure
Tool 14 - Surveying water resources and infrastructure
Tool 15 - Identification of water access constraints
Tool 16 - Data collection on Life-Cycle Costs
Tool 17 - Estimating the benefits of services
2. Situational assessment

## Slide 11
Objective
To agree on a common vision and development of a strategic plan for multiple-use water service provision, which addresses people’s multiple water needs taking into account gender and equity issues of multiple use services.
Activities
Developing a common vision
Setting the levels of access that are needed
Developing strategies for achieving the vision: putting the options on the table
Assessing and prioritising strategies
3. Visioning and strategic planning

## Slide 12
Tools
Tool 18 - MUS Visioning
Tool 19 - Strategy development
Tool 20 - Selection of technologies for multiple uses
Service ladders
3. Visioning and strategic planning

## Slide 13: Levels of access
Scale of activities depend on access to services
  Distance
  Quantity
  Reliability
  (Quantity)
No services
Highest-level Multiple use services
Intermediate-level Multiple use services
Basic-level multiple use services
Basic domestic
Water services sufficient to support most domestic and productive needs
Water services sufficient to support many domestic and productive needs
Water services sufficient to support domestic and limited productive needs
Water services sufficient to meet basic domestic needs only
Level 0
Level 1
Level 2
Level 3
Level 4

## Slide 14: Water ladder
Notes: Need some notes here as a commentary on this. See also query in final column

## Slide 15: Technology options
Different infrastructure systems provide different levels of potential for MUS
  Private options
  Communal systems with single access point
  Communal distribution systems
Incremental steps within and between these system types

## Slide 16: Technology options
Private options
  Family wells
    good access due to close proximity
    may be upgraded with additional lifting devices
  Rainwater harvesting
    often used as a complementary source

## Slide 17: Technology options
Communal point source systems
  Borehole with handpump
    limited productive use at homestead
    at best offers an opportunity for communal productive use
    often used in combination with other sources
  Piped system with scattered standpipes
    has similar limited potential as borehole with handpump

## Slide 18: Technology options
Communal distribution systems (piped or open canal) with supply at the site of use:
  The closer the taps to home, the greater the productive use
  ‘add-ons’:
    Steps in canal
    Rainwater harvesting supplements supply
    Cattle drink from open streams
    Other components to facilitate access – household storage tanks, cattle troughs
    Storage

## Slide 19: Technology options
Potable water treatment often said to result in “wasting clean water on productive uses?”
Mainly an issue in surface water systems
Level of treatment: central or household
Quality of water difficult to achieve, and often has low priority from users
Reuse of wastewater

## Slide 20
Objective
to match costs and financing frameworks while overcoming the earmarks for single water use that are often attached to financing streams and accountability in conventional water services.
Activities
Identify (incremental) life-cycle costs of the provision of multiple use water services
Identify potential sources of funding in order to meet the life-cycle costs
Agree on cost sharing arrangements
4. Fitting the financial framework

## Slide 21: Costs and sources of funding
Incremental costs of MUS include:
Capital (maintenance) expenditure of the technological add-ons such as a water treatment system added to an open canal irrigation system (irrigation +) or a drip irrigation system added to a piped water supply system (domestic +);
Additional operational and minor maintenance related to additional water use because of additional energy consumption;
Additional costs of capital, related to additional loans;
Additional direct and indirect support costs, related with the higher need for coordination between different sub-sectors, which comes at additional costs.
Sources of funding:
Government funding, through taxes
Tariffs (from users)
Transfers from donors

## Slide 22: Costs, and benefits
Stepping up the ladder may cost more
But:
  Allows for economies of scale
  High return on investment, both financial and economical
Possibility to raise leverage investment and operation and maintenance funds

## Slide 23
Tools:
Tool 16 - Data collection on Life-Cycle Costs
Tool 17 - Estimating the benefits of services
4. Fitting the financial framework

## Slide 24
Objective
The objective of this step is to implement the strategic plan as developed in the previous step.
Activities
Development and execution of a work plan / action plan
Infrastructural interventions
Governance and managerial interventions
5. Implementation of MUS interventions

## Slide 25
Tools:
Tool 21 - Training of (community level) service providers
5. Implementation of MUS interventions

## Slide 26
Objective
The objective of this phase is to ensure the continuous provision of sustainable multiple water services.
Activities
Continuous post-construction support (capacity development, technical assistance, facilitation) to service providers and users.
Monitoring
6. Support to continuous service provision

## Slide 27
Tools:
Tool 21 - Training of (community level) service providers
Tool 22 - Monitoring
6. Support to continuous service provision

## Slide 28: A: Evidence-based advocacy on potential and barriers of MUS
Objective
to improve awareness of and insight into the potential and barriers for multiple-use water services of stakeholders at national and intermediate levels within a certain context
Activities
Data collection and analysis to feed evidence based advocacy for MUS
Developing and distributing evidence-based information and advocacy materials

## Slide 29: A: Evidence-based advocacy on potential and barriers of MUS
Tools
Tool 4 - Identification of users of multiple water use services
Tool 16 – Data collection on Life-Cycle Costs
Tool 17 - Estimating the benefits of services
Tool 23 - Actor and task analysis

## Slide 30: B: Capacity development at district and national level
Objective
to create skills, knowledge and attitude and organisational and institutional systems and structures at intermediate and nation level, to stimulate, facilitate and support the provision of multiple-use water services.
Activities
Participatory action research
Training of intermediate and national level stakeholders
Applying a learning alliance approach

## Slide 31: B: Capacity development at district and national level
Tools
Tool 24 - Set-up and facilitation of a learning alliance