## Slide 1
1
GROUNDWATER ANALYSIS TOOL — HANDOVER TRAINING
Session 1
The Big Picture & First Steps
الصورة الكاملة والخطوات الأولى
Tool demo · architecture · accounts · your first Earth Engine map
Colab · Earth Engine · GitHub · Streamlit Cloud

## Slide 2
Today
جدول اليوم
1
2
How it works — the 4 free cloud services
3
Accounts check — everyone ready
Live demo — the dashboards for Jordan, Iraq & Palestine

## Slide 3
Why this tool?
لماذا هذه الأداة؟
Groundwater pumping for irrigation is invisible — no meters, no reports. But the water crops consume is visible from space.
20 m
pixel size — field-level detail
96
months of data (2018–2025)
3
outputs: abstraction (mm, m³) & recharge
0
software installations needed
Satellite inputs: FAO WaPOR v3 (AETI & Or RET) + CHIRPS (rainfall) + GEE (OpenLandMap) — free and updated monthly.
Modeling: Saxton & Rawls equations (soil hydraulics), Thornthwaite-Mather (recharge), FAO (SWB)

## Slide 4
How it works — 4 free services
كيف تعمل — ٤ خدمات مجانية
Google Colab
You run notebooks in the browser
the control room
→
Earth Engine
Stores satellite data & computes the model
the engine
→
GitHub
Holds the dashboard code
the code home
→
Streamlit Cloud
Serves the public dashboard
the screen
Key idea: your computer only sends instructions. All heavy work happens on Google's servers — a normal laptop and a browser are enough.
Repository: github.com/El-Naggar8876/groundwater-tool-handover

## Slide 5
The four accounts you need
الحسابات الأربعة المطلوبة
1
Google + Earth Engine
code.earthengine.google.com/register — choose Unpaid / Academia. Write down your project ID!
may take 1 day for approval
2
Google Colab
colab.research.google.com — same Google account, nothing to install
works immediately
3
GitHub
github.com/signup — pick a professional username
works immediately
4
Streamlit Cloud
share.streamlit.io — sign up WITH your GitHub account
the link matters!
Full walkthrough: docs/00_prerequisites

## Slide 6
Create your GitHub account — step by step
أنشئ حساب GitHub — خطوة بخطوة
1
github.com/signup → enter your email (institutional if possible) → Continue.
2
Password & username. Choose a PROFESSIONAL username — it appears in your public app links (mowr-gw-unit ✓, dragon_king_99 ✗).
3
Verify. Solve the small puzzle, then enter the code GitHub emails you.
4
Skip the questions. “Skip personalization” at the bottom is fine.
5
Done. No Git installation, no command line — ever. Everything happens on the github.com website.

## Slide 7
Register for Earth Engine — step by step
سجّل في محرك الأرض — خطوة بخطوة
1
code.earthengine.google.com/register signed in with your Google account.
2
Unpaid usage → Academia & Research (or Government) → Next.
3
Create a new Cloud project. Project-ID e.g. gw-tool-jordan-moa — lowercase, permanent, CANNOT be changed later.
4
WRITE THE PROJECT ID DOWN. You will type it in every notebook. Accept the Cloud Terms if a banner asks.
5
Test: code.earthengine.google.com opens without an error banner → you are registered (approval can take up to 24 h).
Do this FIRST — approval may take a day. The other three accounts work instantly.

## Slide 8
What is Google Earth Engine?
ما هو محرك جوجل الأرضي؟
A cloud platform holding petabytes of satellite data — CHIRPS rainfall, soil maps, and much more, ready to use
You write small Python commands; Google's servers do the computation
Results come back as maps, numbers, or files — only when you ask (getInfo / export)
Your outputs are stored as “assets” in your own project — like a private data drive
import ee
ee.Authenticate()
ee.Initialize(project="gw-tool-jordan")
rain = (ee.ImageCollection(
"UCSB-CHG/CHIRPS/DAILY")
.filterDate("2023-01-01",
"2024-01-01").sum())
This is the first cell of every notebook — only the project ID changes.

## Slide 9
Before next session
قبل الجلسة القادمة
Finish Notebook 1 incl. exercises — bring one screenshot of your map
Confirm all four accounts work (checklist in docs/00_prerequisites)
Write down: your Earth Engine project ID
NEXT Session 2 — The WaPOR data pipeline: satellite data without downloading a single file