## Slide 1
3
GROUNDWATER ANALYSIS TOOL — HANDOVER TRAINING
Session 3
The Groundwater Model
نموذج المياه الجوفية
Abstraction & recharge · assumptions · running it for your own area
Colab · Earth Engine · GitHub · Streamlit Cloud

## Slide 2
The water balance idea
فكرة الميزان المائي
RAIN (CHIRPS)
what falls
→
EFFECTIVE RAIN
what enters the soil
→
CROP USE (WaPOR AETI)
what plants consume
→
RECHARGE / ABSTRACTION
what is left / what is pumped
In arid irrigated areas: crops consume far more water than rain provides. The difference is pumped from the aquifer — so evapotranspiration measured from space reveals the pumping.

## Slide 3
Four formulas — the whole model
أربع معادلات — النموذج كله
Output | Formula | Unit
Abstraction (mm) | SWB | mm/month
Abstraction (m³) | abstraction_mm × 400 m² ÷ 1000 (per 20 m pixel) | m³/month
Effective rain | P > 75 → 0.8·P − 25 P ≤ 75 → 0.6·P − 10 (FAO, min 0) | mm/month
Recharge | max( effective rain − AETI , 0 ) | mm/month
Everything else in Notebook 3 is plumbing: reading inputs, looping months, exporting results.

## Slide 4
The honest slide — assumptions & limits
شريحة الصراحة — الافتراضات والحدود
!
Assumes ALL crop water comes from groundwater — valid in hyper-arid zones; check areas with rivers or springs
!
Irrigation efficiency is an assumption — replace with local field data when you have it
!
Recharge = potential diffuse recharge only — wadi floods and lateral flows are not included
!
CHIRPS rainfall pixel ≈ 5 km — much coarser than the 20 m WaPOR data
Present results as estimates for planning — not as billing-grade measurements.

## Slide 5
Output names — the contract with the dashboard
أسماء المخرجات — العقد مع لوحة المعلومات
projects/<your-project>/assets/GW_Analysis_<Area>/
abstraction_mm_2023_06 abstraction_m3_2023_06 recharge_2023_06
The dashboard finds months by reading these names — change the pattern and the app shows nothing
Notebook 3 produces exactly this pattern automatically
Safe re-runs: existing outputs are skipped, only new months are computed

## Slide 6
Hands-on — Notebooks 3 & 4
تطبيق عملي — الدفتران ٣ و٤
1
Configure Notebook 3: project ID, REGION, start/end month (start small: one year), output folder name.
2
Run the test cell. Check the min/mean/max of one month look sensible before exporting everything.
3
Start the exports. 3 tasks per month; watch progress at code.earthengine.google.com/tasks.
4
While tasks run: discuss the assumptions slide — which ones matter most in your area?
5
Verify with Notebook 4: inventory, missing months, maps, seasonal chart.

## Slide 7
Before next session
قبل الجلسة القادمة
Extend your run to the full period (exports continue unattended)
Run Notebook 4 and save the seasonal chart — bring it next session
Sanity question: does abstraction peak in the right months for your crops?
NEXT Session 4 — The dashboard: your results live on the internet